## Slide 1: Intel SGX Explained 6.2 Memory Access Protection
Seehwan Yoo
Dankook University

## Slide 2: 6.2 SGX Memory access protection
Isolating enclave from the other memory regions
  Also, isolate enclave from another enclave
MEE plays an role, but not the core protection mechanism
  MEE is at the memory controller, an edge of memory hierarchy
Memory access checks is the core
  Non-enclave software can access outside PRM
  Code inside enclave can access non-PRM
  EPC pages owned by the enclave
  Memory access check is conducted when PMH (page miss handler) works, which only handles TLB miss

## Slide 3: 6.2.1 Functional description
Page table mgmt. in OS; it cannot trust the SW to set up the page tables in any particular way
  Address translation can be rejected before it reaches TLB
All SW uses virtual address, all the micro-ops use virtual addresses
  Handled by TLB before the actual memory access
  By contrast, CPU’s microcode has the ability to issue physical memory access, which bypass the TLB
  SGX uses microcode, so they can bypass TLB, and access memory such as EPC page holding SECS
SGX address translation checks use the information in EPCM (enclave page cache map)
  Inverted page table that covers the entire EPC

## Slide 4: Security checks in enclave mode
First, VA inside enclave virtual memory range (ELRANGE) must be translated into PA inside EPC
  If we are in enclave VA, the corresponding PA should be under EPC
  SGX disallow having enclave code outside ELRANGE (set XD on TLB entry)
Second, EPC must only be accessed by the enclave who owns the page
  SECS page index inside EPC: enclave id (CR_ACTIVE_SECS, microcode register)
  EPCM entry has enclave id; compare with the current enclave id
Third, some EPC cannot be accessed from software
  SECS, TCS, VA (hardware-defined structure) only be accessed by SGX microcode
  PMH rejects address translation targeting these pages
  Blocked EPC: swap-outed process pages
  EPC pages must be accessed using the VA associate with them
    EADD.LINADDR:  EPCM.LINADDR == faulting addr

## Slide 5: PMH modifications for SGX

## Slide 6: 3 implementation options
Checking logic can be implemented
All in microcode
  Least HW modification
  All PMH goes through microcode checking logic
Some in HW register ELRANGE + in microcode
  Better in terms of performance (PMH outside enclave do not touch microcode)
  Rare cases to run outside the enclave
All in HW
  Best performance, but
  Gain is not so dramatic (TLB miss is infrequent)
  Leads to page fault handler and AEX(async. Enc. Exit) to be the bottltneck in performance

## Slide 7: Security check - correctness
At all times all the TLB entries in every logical processor will be consistent with SGX＇s security guarantee
  Assure that all the memory access by software obey SGX＇s security model
Top-level invariants breakdown
  Logical processor (LP) is outside the enclave, ELRANGE to be empty
    Inv.1: At all times when LP is outside enclave mode, its TLB may only contain physical address belonging to DRAM pages outside PRM
    Inv. 2: At all times when LP is inside enclave mode, the TLB entries for virtual address outside the current enclave＇s ELRANGE must contain physical addresses belonging to DRAM pages outside PRM
    Inv. 3: At all times when LP is in enclave mode, the TLB entries for VA inside the current enclave＇s ELRANGE must match the virtual memory layout specified by the enclave author

## Slide 8: Top-level invariants breakdown
Enclave   non-enclave mode transition (at a few well-defined points)
  EENTER, ERESUME, EEXIT and AEX
  Flush TLB and OoO pipeline: TLB empty after every mode transition
Initialization
  Loading some MSR triggers TLB flush
  When modifying MTRR, TLB flush
  Enabling SGX  Adding MTRR  TLB flush, OoO pipeline flush

## Slide 9: Top-level invariants proofs
Inv. 1 proof
  LP is outside enclave mode, SGX security checks added to the PMH reject any addr translation that would point into the PRM before it reaches the TLB
    PRM never changes after SGX is enabled on LP
Inv. 2 proof
  While an LP is executing an enclave code, SGX memory access checks added to PMH reject any addr translation to physical addr inside PRM if VA falls outside the current enclave＇s ELRANGE
    ELRANGE change TLB flush : empty TLB satisfies inv.
Inv. 3 proof
  EPCM (EPC map) virtual memory layout given by the enclave author
    Sub-inv 1. At all times, each EPCM entry matches virtual mem layout desired by the enclave author
    Sub-inv 2. Assume EPCM is constant, at all times when LP is in enclave mode, the TLB entry for VA inside the current enclave ELRANGE must match EPCM entries that belong to the enclave

## Slide 10: Top-level invariants proofs
Inv. 3 proof
  EPCM (EPC map) virtual memory layout given by the enclave author
    Sub-inv 1. At all times, each EPCM entry matches virtual mem layout desired by the enclave author
    Sub-inv 2. Assume EPCM is constant, at all times when LP is in enclave mode, the TLB entry for VA inside the current enclave ELRANGE must match EPCM entries that belong to the enclave
    Sub-inv 3. An EPCM entry is only modified when there is no mapping for it in any LP＇s TLB
  Inv. 2, 3 prove that all the TLBs in SGX-enabled computer always reflect the content of the EPCM
    EPCM is a bridge between the memory layout specification of the enclave authors and TLB entries

## Slide 11: EPCM entries reflect enclave author design
Proof outline for inv3.
  All instructions that modify EPCM pages allocated to an enclave are synchronized using a lock in the enclave SECS (time-ordered)
  EPCM entry created by instructions that can only be issued before EINIT
    Between ECREATE and EADD(?) EINIT
  Contents of the EPCM entry (by the instructions) contributes to the enclave measurement
  Accord. SDM, enclave with incorrect measurement do not exist, as it will be rejected by software attestation
  EPCM pages match enclave author＇s memory layout spec
  EPCM entries can be evicted to untrusted DRAM, together with corresponding EPC pages by EWB instruction (ELDU/ELDB for re-loading)
  If we can prove that EPCM entry that is reloaded from DRAM is equivalent to the evicted entry, then reloaded entry matches the author＇s spec

## Slide 12: EPCM entries reflect enclave author design
evicted EPC page contents and associated metadata has to be protected
  Out of the scope of the work
Evicted page AES-GMAC
  MAC tag by AES-GMAC covers EPCM metadata as well as page date
  Includes 64-bit version stored in a version tree whose nodes are version array pages
It follows that EWB will only reload EPCM entry if the contents is equivalent to the evicted entry
  Equivalence does not mean perfect equality, allowing evicting EPC page, assoc. EPCM entry
  Reloading the page contents to a different EPC page, and fills in different EPCM entry
  Loading the contents of EPC page at different physical address does not break VM abstraction (as long as the page is mapped at the same VA, EPCM.LINADDR, and access control attributes

## Slide 13: Addr translation attacks prevented by MAC verification
ELDU / ELDB
  MAC cover the contents of the evicted EPC page
  MAC covers metadata for EPCM entry
  EID is covered by the MAC tag (enclave1＇s page cannot migrate to another enclave)
  LINADDR is covered by the MAC tag (OS cannot modify virtual memory layout)
  Page access permission is covered by the MAC tag
  Nonce stored in the VA is covered by the MAC tag (OS cannot replay attack, reverts the contents of EPC page to an old version)